## Slide 1: High Precision Urban and Indoor Positioning for Public Safety
NextNav LLC

## Slide 2: Positioning Technology State of Affairs
The missing piece....
5m
50m
500m
Outdoors
Indoors
Urban
Canyon
Accuracy
Areas of Use
A-GPS
A-GPS + AFLT
Cell-ID
Performance Improvements
Needed for Public Safety location:
Indoor/Urban Canyon High Precision
Floor level Vertical Accuracy
Ubiquitous, reliable availability
Wi-Fi

## Slide 3: What Is The Ideal Solution?
High accuracy in urban and indoor environments
High reliability, high yield and pervasive coverage (ubiquitous scale)
Low time to first fix and reduced power drain
On-device location computation (personal privacy)
Minimal device, core network impact and application impact
A terrestrially-based positioning constellation, compatible with GPS, would satisfy all of these requirements

## Slide 4: Deployment Status – Initial 40 Markets
Initial deployment complete in top 39 licensed EAs
40th EA (Orlando) waiting on power at one site (nesting eagle)
Average population coverage exceeds 45 percent in top 40 EAs
Complete & On-air (39 EAs)
Complete, Pending Power (1 EA)
Licensed Markets (115 EAs)

## Slide 5: Mobile Wireless Location: A Brief Background
Mass-market wireless geo-location for wireless devices grew out of FCC requirements for E911
The original Phase II wireless E911 location rules were conceived in 1996 and ultimately promulgated in 2001, when cellphones were secondary communications devices
In 2011, the FCC explicitly clarified that their location accuracy standards apply to outdoor calls only, even as indoor mobile use was dramatically accelerating
The net effect on the wireless location ecosystem has been broad:
  Technologies that work reliably over large geographies are optimized for outdoor positioning
  Technologies that work indoors tend to lack either reliability, coverage, performance or features
This has affected the availability of services for other applications, such as out-of-vehicle officer location
Public Safety location has benefited from the mass-market created by GPS-based consumer location (for outdoor location)

## Slide 6: E911 Now Dominated by Wireless Users
According to the FCC, 70% of 911 calls are placed from wireless phones with some jurisdictions reporting figures over 80%
The most recent data from the Center for Disease Control’s wireless substitution survey indicate that 34% of U.S. homes have only cellular wireless telephones(1)
  Up from approximately 3% in 2003
  56% of renters today are “wireless only” users
An additional 16% of households are “wireless mostly” – using wireless devices for all or nearly all voice communications despite the presence of a land line
(1) http://www.cdc.gov/nchs/data/nhis/earlyrelease/wireless201206.pdf.

## Slide 7: Indoor E911 Process at the FCC
The FCC established CSRIC 3, Working Group 3 to examine and make recommendations on indoor location accuracy standards
  Group includes regulatory, public safety, carrier and industry participation
CSRIC3, WG3 recommended that a “real world” test program be conducted to inform any future rule-making for indoor location accuracy standards
  Independent third-party testing conducted in San Francisco Bay Area through Q412
  Final report presented and approved by CSRIC March 14, 2013
Effect on ecosystem will be to bring reliable, accurate indoor wireless geo-location, suitable for safety services, into the mass-market for the first time
Bay Area Test Network
CSRIC Indoor Location Recommendations and Final Report
Indoor Location NPRM
Indoor Location Report & Order
Q4 2012
March 2013
2013
TBD
Indoor Location Accuracy Process

## Slide 8: Test Area Summary
Dense Urban – Downtown SF
Urban – Downtown SF
Urban – San Jose
Suburban – Santa Clara County
Rural - Hollister

## Slide 9: Summary Results-- Accuracy
Urban environment had the most challenged horizontal accuracy followed closely by dense urban
NextNav technology provided vertical results
CSR C
Communications Security, Reliability and Interoperability Council

## Slide 10: FCC Sponsored CSRIC Trial

## Slide 11: Existing E911 Rules (Outdoor)
~150m
~50m

## Slide 12: In-Building Requires High Performance Location – and Height
50m
Across all morphologies, in the CSRIC test bed NextNav delivered 37m of accuracy (population-weighted) 67% of the time and was able to identify the building or an adjacent building over 80% of the time.
In the CSIRC test bed, NextNav delivered floor-level precision, with median vertical accuracy of 2 meters.

## Slide 13: Floor-Level Height Accuracy
NextNav is building the nation’s first high precision, real time barometric pressure calibration network

## Slide 14: NextNav Tracking Performance – Westfield Valley Fair
Walking test result in Valley Fair Mall, ground-truth (red) compared with NextNav measurements (green)

## Slide 15: Public Safety Forward to CSRIC WGIII Report
"Public Safety desires reliable and consistent caller location information to a specific dispatch-able building (and floor in multi-story environments). Lacking the specific building and floor, the desire would be for the smallest possible search ring…
…Horizontal positional fixes that substantially exceed 50 meter accuracy provide only general location information. Tighter performance is required, particularly in urban and dense urban environments to narrow the search ring to a single building or a more reasonable number of adjacent buildings…
… emerging technologies demonstrate the ability to achieve improved search rings in the horizontal dimension (often identifying the target building, or those immediately adjacent). Substantial progress in the vertical dimension (67th percentile of 2.9 meters, or approximate floor level accuracy) was also demonstrated by one emerging technology… such functionality would be an important factor in locating indoor callers in urban and dense urban multistory buildings.”

## Slide 16: Summary
The CSRIC Test Bed has proven that multiple high yield, high reliability technologies are available to provide E911 Phase II indoor location, but location accuracy varies significantly between technologies.
Outdoor location standards (50m/150m) are inadequate for indoor location in urban environments, since search rings significantly larger than 50m cannot consistently identify dispatch-able building locations.
Emerging technologies (NextNav) substantially reduce search ring area (by 10X) over existing technologies, and provide floor level vertical accuracy in multi-floor buildings.
NextNav is deploying a “carrier grade” wide-area positioning network to dramatically improve indoor/urban location capabilities for E911 and Public Safety first responders